## Slide 1
15EC502 – Linear Integrated Circuits

## Slide 2
UNIT I - IC FABRICATION AND CIRCUIT CONFIGURATION FOR LINEAR ICS
Advantages of ICs over discrete components
Manufacturing process of monolithic ICs
    bipolar transistor
    diodes
    Integrated Resistors
    Capacitors
    Inductors.
Differential gain – CMRR
General operational amplifier stages
    Internal circuit diagrams of IC 741
DC and AC performance characteristics
    Slew rate
Open and closed loop configurations

## Slide 3
Advantages of ICs over discrete components
Miniaturization and hence increased equipment density
Cost reduction due to batch processing
Increased system reliability due to elimination of soldered joints
Improved functional performance.
Matched devices.
Increased operating speeds.
Reduction in power consumption.
packaged ICs use much less material than discrete circuits
Uniformity of components
Ease of manufacture
Speed, Size, Cost, Power Consumption improvement
More robust against vibration

## Slide 4
Basic Information of Op-Amp
Op-Amp Symbol

## Slide 5
Basic Information of Op-Amp
Packages
The Metal Can (TO) Package
The Dual-in-line Package
The Flat package or Flat pack

## Slide 6
Basic Information of Op-Amp
Package may contain Single, Two (Dual) or Four (Quad) Op-Amps
Number of pins (8 – CAN, DIP; 10 - Flat; 14 – IP)

## Slide 7
Basic Information of Op-Amp
Op-Amp Terminals

## Slide 8
Basic Information of Op-Amp
Op-Amp Power Supply Connections
Gnd is Must, otherwise twice the supply damage the Op-Amp.

## Slide 9
Basic Information of Op-Amp
Op-Amp Power Supply Connections
Instead of single power supply,
  Use resistive divider
  Use Zener Diodes
  Use of Potentiometer and Diodes.

## Slide 10
Basic Information of Op-Amp
Op-Amp Manufacturers
Fairchild - µA, µAF
National Semiconductor - LM, LH, LF, TBA
Motorola - MC, MFC
RCA - CA, CD
Texas Instruments - SN
Signetics - N/S, NE/SE
Burr/Brown - BB
Op-Amp Numbers will end up with 741 (Ex.: LM 741)

## Slide 11
Basic Information of Op-Amp
Op-Amp Manufactured for….
741 - Military Purpose (Temp. -55°C - 125°C)
741C - Commercial (Temp. 0°C - 75°C)
741A - Improved version of 741
741E - Improved version of 741C
741S - Military with High Slew-Rate
741SC - Commercial with High Slew-Rate
Electrical Properties

## Slide 12
Fabrication Process
Silicon Wafer Preparation
Epitaxial Growth
Oxidation
Photolithography
Diffusion
Ion Implantation
Isolation Techniques
Metallization
Assembling and Packaging
I. Basic Planar Fabrication Process
II. Fabrication Process of a Circuit
III. Fabrication Process of Active and Passive Elements
Transistors (BJT and FET)
Diode
Resistors
Capacitors
Inductors

## Slide 13
Fabrication Process

## Slide 14
Fabrication Process

## Slide 15
Fabrication Process
Basic Planar Fabrication Process :
Silicon Wafer Preparation

## Slide 16
Fabrication Process
Basic Planar Fabrication Process :
Silicon Wafer Preparation

## Slide 17
Fabrication Process
Basic Planar Fabrication Process :
Silicon Wafer Preparation

## Slide 18
Fabrication Process
Basic Planar Fabrication Process :
Silicon Wafer Preparation

## Slide 19
Fabrication Process
Basic Planar Fabrication Process :
Silicon Wafer Preparation

## Slide 20
Fabrication Process
Basic Planar Fabrication Process :
Epitaxial Growth

## Slide 21
Fabrication Process
Basic Planar Fabrication Process :
Oxidation

## Slide 22
Fabrication Process
Basic Planar Fabrication Process :
Photolithography

## Slide 23
Fabrication Process
Basic Planar Fabrication Process :
Photolithography

## Slide 24
Fabrication Process
Basic Planar Fabrication Process :
Photolithography

## Slide 25
Fabrication Process
Basic Planar Fabrication Process :
Diffusion Process

## Slide 26
Fabrication Process
Basic Planar Fabrication Process :
Diffusion Process

## Slide 27
Fabrication Process
Basic Planar Fabrication Process :
Ion Implantation

## Slide 28
Fabrication Process
Basic Planar Fabrication Process :
Ion Implantation

## Slide 29
Fabrication Process
Basic Planar Fabrication Process :
Isolation Technique – PN Junction Isolation

## Slide 30
Fabrication Process
Basic Planar Fabrication Process :
Isolation Technique – PN Junction Isolation

## Slide 31
Fabrication Process
Basic Planar Fabrication Process :
Isolation Technique – PN Junction Isolation

## Slide 32
Fabrication Process
Basic Planar Fabrication Process :
Isolation Technique – Dielectric Isolation

## Slide 33
Fabrication Process
Basic Planar Fabrication Process :
Isolation Technique – Dielectric Isolation

## Slide 34
Fabrication Process
Basic Planar Fabrication Process :
Metallization

## Slide 35
Fabrication Process
Basic Planar Fabrication Process :
Metallization

## Slide 36
Fabrication Process
Basic Planar Fabrication Process :
Metallization

## Slide 37
Fabrication Process
Basic Planar Fabrication Process :
Assembling and Packaging

## Slide 38
Fabrication Process
Basic Planar Fabrication Process :
Assembling and Packaging

## Slide 39
Fabrication Process
Fabrication Process of a Circuit:

## Slide 40
Fabrication Process
Fabrication Process of a Circuit:
Wafer Preparation

## Slide 41
Fabrication Process
Fabrication Process of a Circuit:
Epitaxial Growth

## Slide 42
Fabrication Process
Fabrication Process of a Circuit:
Oxidation

## Slide 43
Fabrication Process
Fabrication Process of a Circuit:
Isolation Diffusion
Isolation Diffusion – Top View

## Slide 44
Fabrication Process
Fabrication Process of a Circuit:
Base Diffusion

## Slide 45
Fabrication Process
Fabrication Process of a Circuit:
Emitter Diffusion

## Slide 46
Fabrication Process
Fabrication Process of a Circuit:
Emitter Diffusion – Top View

## Slide 47
Fabrication Process
Fabrication Process of a Circuit:
Aluminium Metallization

## Slide 48
Fabrication Process
Fabrication Process of a Circuit:
Aluminium Metallization

## Slide 49
Fabrication Process
Fabrication Process of a Circuit:
Cross-sectional View

## Slide 50
Fabrication Process
Fabrication Process of a Circuit:
Cross-sectional View

## Slide 51: INTEGRATED CAPACITORS AND INDUCTORS

## Slide 52: INTEGRATED CAPACITORS
METHODS:
>Junction Capacitor
>MOS and Thin film Capacitor

## Slide 53: 1] JUNCTION CAPACITOR

## Slide 54: Description
> 2 Junctions J1,J2
> J2 –reverse biased : produces C2(desired capacitance)
> J1-present between n-type layer and substrate : produces C1
>Due to bulk resistance of n-type region there occurs a series resistance R

## Slide 55: Conditions
> To minimize C1,substrate must be held at the most negative point in the circuit.
>Value of C2 depends on:
* Area of the junction
* Impurity concentration of n-type layer.
* Voltage across the junction

## Slide 56: Inference
> C2 is polarized -It can be obtained only when
the junction is reverse biased..
> Therefore, the junction capacitance of a reverse biased diode is used as an element in
monolithic ICs..

## Slide 57: 2]MOS AND THIN FILM CAPACITOR

## Slide 58: MOS
>Parallel plate capacitor
>SiO2 – dielectric
>n-type region : lower plate
>thin film of aluminium
metallization : upper plate
>It consists of a resistance R due to n+ region ,junction J1 and associated capacitance C1

## Slide 59: Inference
>capacitor is non-polar:
The plates can be positive or negative
and it is not a function of voltage applied.
>Silicon Nitride(Si3N4)-can be use as a dielectric layer to give more circuit flexibility.

## Slide 60: THIN FILM CAPACITOR
>Aluminium or tantalum is used as capacitor plates.
>aluminium oxide(Al2O3) or tantalum oxide(Ta2O5) is used as dielectric plates.
>cons:
it fails when voltage rating exceeds due to breakdown of the dielectric.
It is a destructive and irreversible failure mechanism and hence requires voltage protection.

## Slide 61: Comparison
Junction capacitor
Mos capacitor
>The desired capacitance (C2) is polarised.
>It can only be obtained when the junction (J2) is reverse biased.
>It depends upon the applied voltage.
>The capacitor is non-polar.
>the plates can be either positive or negative
>It is not a function of the voltage applied.

## Slide 62: INTEGRATED INDUCTORS
IC inductors can be made into a metallic thin film spirals-by successive deposition of conduction patterns.
Inductance in the order of nano-henry with low quality can only be obtained.
A 3-dimensional coil structure is required to obtain large no.of turns.

## Slide 63: Applications
In RF circuits , inductors external to IC-packages are used.
In thin film MIC , thin- film inductor spirals are used giving upto 250 nH.

## Slide 64: MONOLITHIC DIODES AND SCHOTTKY BARRIER DIODE

## Slide 65: VARIOUS DIODE STRUCTURE:

## Slide 66: TYPICAL VALUES:

## Slide 67: DEFINITION:
Breakdown voltage: It is the maximum voltage that the diode can withstand in reverse bias condition
Storage time: The time period for the diode to remain in the conduction state even in the reverse bias state
Forward Voltage: Voltage drop across the diode in forward bias condition

## Slide 68: Cross section of a monolithic diode:

## Slide 69: OHMIC CONTACT RECTIFYING CONTACT
Diffuse n+ regions over the Al is deposited
Bipolar
Obeys ohms law
Al is directly deposited upon the n type
Unipolar
Forward voltage is 0.3v

## Slide 70: VI CHARACTERISTICS:

## Slide 71: SCHOTTKY DIODE:

## Slide 72: FEATURES OF SCHOTTKY DIODE:
Hot Carrier Diode
Metal and semiconductor junctions
Electrons as a majority carrier
No depletion region is formed
Reverse Recovery time is less
Low Forward voltage drop (0.3v)
Used in low power applications
Used in high switching applications like microwave Ics,detectors,clampers.

## Slide 73
Ideal Op-Amp Characteristics
Vd = 0

## Slide 74
Characteristic | Value
Open Loop Gain (AOL) | ∝
Input Resistance (Ri) | ∝
Output Resistance (Ro) | 0
Bandwidth of Operation (BW) | ∝
Offset Voltage (V0= 0; when V1=V2= 0) | 0
Ideal Op-Amp Characteristics

## Slide 75
Ideal Op-Amp Equivalent Circuit

## Slide 76
Op-Amp Open Loop

## Slide 77
Op-Amp Closed Loop
Current drawn by either of the input terminals is negligible.
The differential input voltage Vd is essentially Zero.
The Output Voltage (V0) is independent of current drawn from output (as R0 = 0).
V0 = AOL.Vd = AOL. (V1-V2)
Assumptions

## Slide 78
Op-Amp Closed Loop
Configurations
Inverting Amplifier
Non-Inverting Amplifier
Voltage Follower
Differential Amplifier

## Slide 79
Op-Amp Closed Loop
Inverting Amplifier
No Current Flows into the Input Terminals
The Differential Input Voltage is Zero as V1 = V2 = 0 (Virtual Ground)

## Slide 80
Op-Amp Closed Loop
Inverting Amplifier
Closed-Loop Voltage Gain is,

## Slide 81
Problem
Design an Amplifier with a gain of -10 and input resistance equal to 10kΩ..
Solution:
  Given
  Gain = -10
  Ri = 10kΩ

## Slide 82
Problem
Design an Amplifier with a gain of -10 and input resistance equal to 10kΩ.
Solution:
  Given
  Gain = -10
  Ri = 10kΩ
Rf = -ACL Ri = - (10)×(10kΩ) = 100kΩ

## Slide 83
Problem
In an Inverting Amplifier, R1= 10kΩ , Rf= 100kΩ, Vi=1V. A load of 25kΩ is connected to the output terminal. Calculate,
i1, V0, iL, and Total Current i0?
Solution:
Given
  R1= 10kΩ ,
  Rf= 100kΩ,
  Vi=1V,
  A load of 25kΩ

## Slide 84
Problem

## Slide 85
Op-Amp Closed Loop
Non-Inverting Amplifier
No Current Flows into the Input Terminals
The Vd Differential Input Voltage is Zero. Hence, Potential at V1 = Vi

## Slide 86
Op-Amp Closed Loop
Non - Inverting Amplifier
Closed-Loop Voltage Gain is,

## Slide 87
Problem
Design an Amplifier with a gain of +5 using an Op-Amp.
Solution:
  Given
  Gain = +5

## Slide 88
Problem
Design an Amplifier with a gain of +5 using an Op-Amp.
Solution:
  Given
  Gain = +5
  Assume, R1 = 10kΩ
  ACL = (1+ (Rf/R1)) => 5 = 1+ (Rf/R1) =>
  Rf = 40kΩ

## Slide 89
Problem
In an Non-Inverting Amplifier, R1= 5kΩ , Rf= 20kΩ, Vi=1V. A load of 5kΩ is connected to the output terminal. Calculate,
V0, ACL, iL, Total Current i0 and direction of flow?
Solution:
  Given
  R1= 5kΩ ,
  Rf= 20kΩ,
  Vi=1V,
  A load of 5kΩ

## Slide 90
Problem
Solution:
V0=Vi(1+ (Rf/R1)) = 5V
ACL = V0/Vi = 5
iL = V0 / RL = 1mA
i1 = Vi/R1 = V0-Vi = 0.2mA
i0 = iL + i1 = 1.2mA

## Slide 91
Op-Amp Closed Loop
Voltage Follower
Rf=0; Ri=Infinity; Vo=Vi; R0=0
Used for Impedance Matching Circuitry.

## Slide 92
Advantages of Voltage Follower
  Provides power gain and current gain.
  Low output impedance to the circuit which uses the output of the voltage follower.
  The Op-amp takes zero current from the input.
  Loading effects can be avoided.
Applications of Voltage Follower
  Buffers for logic circuits.
  In Sample and hold circuits.
  In Active filters.
  In Bridge circuits via transducer.
Op-Amp Closed Loop
Voltage Follower

## Slide 93
Op-Amp Closed Loop
Differential Amplifier

## Slide 94
Op-Amp Closed Loop
Analysis
At Node ‘a’,
(Va – V1)/R1 + (Va – V0)/R3 = 0 ----- (1)
At Node ‘b’,
(Vb – V2)/R2 + (Vb – 0)/R4 = 0 ----- (2)
In equation (2), put R1=R2 and R3 = R4, and Rearranging,
(1) => Va (1/R1 – 1/R3) – (V1/R1) = V0/R3 ----- (3)
    => Va (1/R1 – 1/R3) – (V2/R1) = 0 (ஃ Va = Vb) ----- (4)
Subtract (3) – (4),
-(V1/R1) + (V2/R1) = V0/R3 ----- (5)
Rearranging the above,
V0 = R3/R1 (V2-V1)
Assume, it is ideal Op-Amp,
Current in to the Op-Amp is Zero.
Vd=0; then, Va=Vb.

## Slide 95
Op-Amp Closed Loop
Differential Amplifier
Consider V1=V2=V3 Find ACL?
R1 = R2 = R3 = R4 then the circuit will become a Unity Gain Differential Amplifier

## Slide 96
Difference Mode and Common Mode Gain
If V1 = V2 => V0 = ‘0’ (ஃ both inputs are cancelled and no output - Ideal)
But, Practically V0 is not Zero for Common Mode.
Case i: V1=100µV & V2=50µV; then V0= V3.
Case ii: V1=1000µV & V2=950µV; then V0= V4.
V3 is not equal to V4; even V1-V2 is same both cases.
Hence, output voltage is dependent on Vd and VCM.
VCM = (V1+V2) / 2
Reason: Components Mismatch

## Slide 97
Difference Mode and Common Mode Gain
Hence, Output Voltage is,
V0 = A1V1 + A2V2 ----(1)
Where, A1 = Gain of Input 1, when input 2 is Grounded.
A2 = Gain of Input 2, when input 1 is Grounded.
Differential mode component : Vd = (V1-V2) Common mode component : Vcm = (V1+V2)/2
Vcm = (V1+V2)/2 ----(2) & 2Vcm = V1 + V2 ---- (3)
Since Vd = V1 - V2 ---- (4)
Therefore
(3) + (4) & V1 = Vcm + Vd/2 ---- (5)
and (3) - (4) & V2 = Vcm - Vd/2 ---- (6)

## Slide 98
Difference Mode and Common Mode Gain
Sub. (5), (6) in eqn. (1), we get,
V0 = ADM Vd + ACM VCM.
Where,
Difference Mode Gain ADM = (1/2)(A1 – A2)
Common Mode Gain ACM = A1+A2
Hence, Common-Mode Rejection Ratio (CMRR) is,
CMRR (ρ) = | ADM / ACM |

## Slide 99
Hence, Common-Mode Rejection Ratio (CMRR) is,
CMRR (ρ) = | ADM / ACM |
Common Mode Rejection Ratio
CMMR = Differential mode gain / Common-mode gain
Ref.:: https://www.youtube.com/watch?v=hpCu3HbAiWg
CMRR used to be in the range of 80 to 100 dB
Ideally, ADM is Large and ACM is Zero; So that, CMRR = HIGH (for Good Op-Amp).

## Slide 100
DC Characteristics of Op-Amp
Ideal Op-Amp draws no current from the source and independent of Temperature.
Practically, current is taken from the source into the Op-Amp inputs.
Two inputs respond differently to Current and Voltage due to Mismatch.
Real Op-Amp has dependent on temperature.
Non-Ideal Characteristics are,
  Input Bias Current.
  Input Offset Current
  Input Offset Voltage
  Thermal Drift

## Slide 101
1. Input Bias Current
The Differential amplifier may be FET or BJT based device.
In Ideal op-amp, we assume no current is drawn by the inputs.
In Practical due to mismatch of components current drawn in both the terminals.
They are named as IB+ and IB-
IB = (IB+ and IB- ) / 2

## Slide 102
1. Input Bias Current
Ex.: if IB = 500nA, Vi = 0, then V0 is,
V0 = (IB- Rf)
if Rf = 100MΩ then,
V0 = 500mV
For BJT this IB is 500nA and for FET IB is 50pA
The output is driven to 500mV with zero input, because of the bias currents.

## Slide 103
1. Input Bias Current (with Rcomp)

## Slide 104
1. Input Bias Current (with Rcomp)
Analysis
Current IB+ flowing through the compensating resistor Rcomp, then by KVL,
-V1+0+V2-Vo = 0 (or) ——>(1)
Vo = V2 – V1 ——>(2)
By selecting proper value of Rcomp, V2 can be cancelled with V1 and the Vo = 0. The value of Rcomp is derived
V1 =IB+Rcomp ——>(3)
IB+ = V1/Rcomp ——>(4)

## Slide 105
1. Input Bias Current (with Rcomp)
The node ‘a‘ is at voltage (-V1). Because the voltage at the non-inverting input terminal is (-V1). So with Vi = 0
I1 = V1/R1 ——>(5)
I2 = V2/Rf ——>(6)
For compensation, Vo should equal to zero (Vo = 0, Vi = 0). i.e. from equation (2) V2 = V1. So that from (6)
I2 = V1/Rf ——>(7)
KCL at node ‘a‘ gives,
IB-= I2 + I1 add eqn, (5) and (7), we get,
IB-= V1 ((R1 + Rf)/RfR1) ——>(8)
Assume IB- = IB+ then from (4) & (8),
Rcomp = ((R1 + Rf)/RfR1) = R1 || Rf

## Slide 106
1. Input Bias Current (with Rcomp)
Analysis
Rcomp = ((R1 + Rf)/RfR1) = R1 || Rf
Ref.: http://www.brainkart.com/article/DC-Characteristics-of-op-amp_13376/

## Slide 107
2. Input Offset Current
Bias current compensation will work if both bias currents IB+ and IB- are equal.
Since the input transistor cannot be made identical. There will always be some small difference between IB+ and IB-. This difference is called the offset current.
|Ios| = IB+ -IB-
Offset current Ios for BJT op-amp is 200nA and for FET op-amp is 10pA. Even with bias current compensation, offset current will produce an output voltage when Vi = 0.
——>(1)

## Slide 108
2. Input Offset Current
V1 =IB+Rcomp ——>(2)
I1 = V1/R1 ——>(3)
KCL at node ‘a‘ gives,
IB-= I2 + I1
——>(4)
I2 = (IB- - I1 )
——>(5)
In (5), use (2) and (3) we get,
I2 = (IB- - (IB+Rcomp /R1)) ——>(6)

## Slide 109
Vo = V2 – V1 ——>(7)
Vo = I2 Rf – V1 = I2 Rf – IB+Rcomp ——>(8)
Sub. (6) in (8) and simplifying we get,
Vo = Rf (IB- – IB+) ——>(9)
Vo = Rf (Ios)
2. Input Offset Current

## Slide 110
2. Input Offset Current
The offset current can be minimized by keeping feedback resistance small.
Unfortunately to obtain high input impedance, R1 must be kept large. R1 large, the feedback resistor Rf must also be high. So as to obtain reasonable gain.
Use T- Network in the feedback is a better solution.

## Slide 111
3. Input Offset Voltage
Inspite of the use of the above compensating techniques, it is found that the output voltage may still not be zero with zero input voltage [Vo ≠ 0 with Vi = 0].

## Slide 112
3. Input Offset Voltage
At node V2 apply nodal equation and find V0?
V0 = V2 (1+(Rf /R1))
——>(1)
Vios = |Vi -V2| and Vi = 0.
——>(2)
From (1) and (2) =>
V0 = Vios (1+(Rf /R1))

## Slide 113
4. Total Output Offset Voltage
The total output offset voltage VOT could be either more or less than the offset voltage produced at the output due to input bias current (IB) or input offset voltage alone(Vos).
This is because IB and Vos could be either positive or negative with respect to ground.
VOT = Vios (1+(Rf /R1)) + Rf (Ios)

## Slide 114
6. Thermal Drift
Bias current, offset current, and offset voltage change with temperature.
A circuit carefully nulled at 25ºC may not remain. So when the temperature rises to 35ºC. This is called drift.
Offset current drift is expressed in nA/ºC or mV/ºC.
These indicate the change in offset for each degree Celsius change in temperature.

## Slide 115
Problem: 1
Problem: 2

## Slide 116
Problem: 1

## Slide 117
Problem: 2

## Slide 118
AC Characteristics
Dominant Pole Compensation
Pole-Zero Compensation
External Compensation:
Internal Compensation:
Op Amp Frequency Response:
Slew Rate

## Slide 119
AC Characteristics
Op Amp Frequency Response:

## Slide 120
z = x + iy
|z| = √(x2 + y2),
z.¯z=(x+iy)(x−iy)=x2+y2
AC Characteristics
Xc = 1/jwc or -j/wc.

## Slide 121
AC Characteristics
Op Amp Frequency Response:

## Slide 122
AC Characteristics
Op Amp Frequency Response:

## Slide 123
AC Characteristics
Op Amp Frequency Response:

## Slide 124
AC Characteristics
Op Amp Frequency Response:

## Slide 125
AC Characteristics
Op Amp Frequency Response:

## Slide 126
AC Characteristics
Frequency Compensation:
Dominant Pole Compensation
Pole-Zero Compensation
I. External Compensation:
II. Internal Compensation:

## Slide 127
AC Characteristics
I. External Compensation: Dominant Pole Compensation

## Slide 128
AC Characteristics
I. External Compensation: Dominant Pole Compensation

## Slide 129
AC Characteristics
I. External Compensation: Dominant Pole Compensation

## Slide 130
AC Characteristics
I. External Compensation: Pole-Zero Compensation

## Slide 131
AC Characteristics
I. External Compensation: Pole-Zero Compensation

## Slide 132
AC Characteristics
I. External Compensation: Pole-Zero Compensation

## Slide 133
AC Characteristics
I. External Compensation: Pole-Zero Compensation

## Slide 134
AC Characteristics
I. External Compensation: Pole-Zero Compensation

## Slide 135
AC Characteristics
II. Internal Compensation:

## Slide 136
AC Characteristics
II. Internal Compensation:

## Slide 137
AC Characteristics
II. Internal Compensation:

## Slide 138
AC Characteristics
Slew Rate
SR is the maximum rate of change of output voltage per unit of time and is expressed in volts per microseconds.
Slew Rate, SR = dVo/dt
In the case of the 741 IC the slew rate is 0.5V/µS, which is very small. This is one reason why the 741 IC is considered not suitable for high frequency applications, such as oscillators, comparators, and filters.
The slew rate is caused due to limited charging rate of the compensation capacitor and current limiting and saturation of the internal stages of op-amp, when a high frequency large amplitude signal is applied.

## Slide 139
It is given by dVc /dt = I/C For large charging rate, the capacitor should be small or the current should be large.
AC Characteristics
Slew Rate
SR = dVc /dt = Imax / C
For 741 IC the charging current is 15 µA and the internal capacitor is 30pF.
      SR= 0.5V/ µsec

## Slide 140
AC Characteristics
Slew Rate

## Slide 141
AC Characteristics
Slew Rate

## Slide 142
AC Characteristics
Slew Rate

## Slide 143
AC Characteristics
Slew Rate

## Slide 144
AC Characteristics
Slew Rate

## Slide 145
AC Characteristics
Slew Rate

## Slide 146
AC Characteristics
Slew Rate

## Slide 147
AC Characteristics
Slew Rate

## Slide 148
AC Characteristics
Slew Rate

## Slide 149
OP-AMP INTERNAL CIRCUIT
General Stages

## Slide 150
Input Stage: The main function of Op Amp is, at first it creates a difference between the two input signals and then amplify the differentiated signal. So in the Input Stage, the differential amplifier creates the differences with high gain. In this stage, the differential amplifier also provides the high input impedance which is necessary for the operational amplifier. You can see in this stage the dual input balanced output differential amplifier is used which increase the voltage for next stage operation.
Intermediate Stage: The output of the input stage is used as the input of the Intermediate Stage. In this stage, the direct coupling happens. So, in this stage, the DC voltage is greater than the ground potential or 0V.
Level Shifting Stage: As in this stage the shifting of DC voltage level happens that is why it is called Level Shifting Stage. Here the emitter follower with a constant current source is applied. Its, input impedance also high.
Output Stage: In this stage, the push-pull amplifier is used. The output of the level shifting stage is given to the input of the push-pull amplifier. The push-pull amplifier increases the output voltage and high current delivering capability of the operational amplifier. The output stage has low impedance.
OP-AMP INTERNAL CIRCUIT
General Stages

## Slide 151
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):

## Slide 152
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
It rejects common mode input
The differential pair with a common-mode input signal vCM.

## Slide 153
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
The differential pair with a “large” differential input signal

## Slide 154
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
The differential pair with a large differential input signal of polarity opposite to that in .

## Slide 155
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
Configurations
Based on the methods of providing input and taking output, differential amplifiers can have four different configurations as below.
  Single Input Unbalanced Output
  Single Input Balanced Output
  Dual Input Unbalanced Output
  Dual Input Balanced Output

## Slide 156
Single Input Unbalanced Output
Single Input Balanced Output
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):

## Slide 157
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
Dual Input Unbalanced Output
Dual Input Balanced Output

## Slide 158
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
--------> (1)
--------> (2)
--------> (3)

## Slide 159
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):
Using the above equations… (2), (3) and (4) we get,
--------> (4)
--------> (5)

## Slide 160
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):

## Slide 161
OP-AMP INTERNAL CIRCUIT
Differential Amplifier (1st and 2nd Stage):

## Slide 162
OP-AMP INTERNAL CIRCUIT

## Slide 163
OP-AMP INTERNAL CIRCUIT
Level Translator
Level shifter or translator is usually connected in a typical Op-Amp so as to shift the D.C. Level at the output of intermediate stage which is grounded onward to zero.
Intermediate stage is basically a differential amplifier which is driven by the previous state output. The D.C. Level at the output of intermediate stage is good above ground potential in case of direct coupling. Hence, it is obligatory to use the level shifter in OP-Amps.
Because of the direct coupling the dc level at the emitter rises from stages to stage. This increase in dc level tends to shift the operating point of the succeeding stages and therefore limits the output voltage swing and may even distort the output signal. To shift the output dc level to zero, level translator circuits are used. An emitter follower with voltage divider is the simplest form of level translator as shown in fig1.1 Thus a dc voltage at the base of Q produces 0V dc at the output. It is decided by R1 and R2. Instead of voltage divider emitter follower either with diode current bias or current mirror bias as shown in fig1.2may be used to get better results. In this case, level shifter, which is common collector amplifier, shifts the level by 0.7V. If this shift is not sufficient, the output may be taken at the junction of two resistors in the emitter leg.

## Slide 164
OP-AMP INTERNAL CIRCUIT
Level Translator

## Slide 165
OP-AMP INTERNAL CIRCUIT
Output Stage
This stage should be capable of supplying load current and should have low output resistance.
Complementary push pull amplifier increases the output voltage swing of the output signal and also increases the current supplying capability of op-amp.

## Slide 166
OP-AMP INTERNAL CIRCUIT
Output Stage

## Slide 167
OP-AMP INTERNAL CIRCUIT

## Slide 168
http://www.brainkart.com/article/Important-Short-Questions-and-Answers--Characteristics-of-op-amp_13381/
http://www.ecircuitcenter.com/RunSPICE.htm
http://www.faadooengineers.com/online-study/post/eee/analog-electronics-circuits/1011/level-translator

## Slide 169
https://www.mepits.com/tutorial/384/vlsi/steps-for-ic-manufacturing