## Slide 1
15EC502 – Linear Integrated Circuits

## Slide 2
UNIT II APPLICATIONS OF OPERATIONAL AMPLIFIERS
Sign Changer
Scale Changer
Voltage Follower
Adder & Subtractor
Instrumentation amplifier
Integrator & Differentiator
Low–pass, High–pass and Band–pass filters
Phase Shift Circuits
Comparators & Schmitt trigger
Multivibrators
Sine–wave generators
Precision rectifier
V to I and I to V converters.

## Slide 3
OP AMP APPLICATIONS
Two types of Applications,
  Linear Applications
  Non-Linear Applications

## Slide 4
  Linear Applications
Addition
Subtraction
Multiplication
Current to Voltage and Voltage to current conversion
Integration
Differentiation
Active Filters
Comparators
Schmitt trigger
Instrumentation Amplifier
F to V converter

## Slide 5
  2. Non-Linear Applications
Comparators
Logarithmic amplifiers
Exponential amplifiers
Peak detectors
Precision rectifiers
Waveform generators
Clippers & clampers

## Slide 6: Inverter and Scale Changer
  Linear Applications
Inverting Amp with Gain = - Rf / Ri
Inverter
  Rf / Ri = 1
Inverter and Scale Changer
  Proper choice of Rf / Ri
Application
  Use of inverter to scale the output of DAC

## Slide 7: Summing Amplifier (Inverting)
  Linear Applications

## Slide 8: Summing Amplifier (Inverting)
  Linear Applications

## Slide 9: Summing Amplifier (Inverting)
  Linear Applications
Problem

## Slide 10: Summing Amplifier (Inverting)
  Linear Applications
Solution

## Slide 11: Summing Amplifier (Inverting)
  Linear Applications
Home Work

## Slide 12: Summing Amplifier (Non - Inverting)
  Linear Applications

## Slide 13: Summing Amplifier (Non - Inverting)
  Linear Applications

## Slide 14: Summing Amplifier (Non - Inverting)
  Linear Applications
Ref.: https://www.youtube.com/watch?v=2cqgg0PPRNg

## Slide 15: Summing Amplifier (Non - Inverting)
  Linear Applications
Home Work
For V1 = 3V and V2 = -4V We get
VOUT = (6 X 3V) - (4 X 4V) = 2V

## Slide 16: Subtractor
  Linear Applications

## Slide 17: Subtractor
  Linear Applications
Use Super Position Principle,

## Slide 18: Adder - Subtractor
  Linear Applications

## Slide 19: Adder - Subtractor
  Linear Applications

## Slide 20: Adder - Subtractor
  Linear Applications
Use Superposition Principle, then
METHOD: 1

## Slide 21: Adder - Subtractor
  Linear Applications
METHOD: 1

## Slide 22: Adder - Subtractor
  Linear Applications
Use Nodal Analysis, then
METHOD: 2
Write Nodal equation at Node ‘a’ (Inverting Terminal)
Write Nodal equation at Node ‘b’ (Non-Inverting Terminal)
Consider, Va = Vb  Va in the above two equations.
Then, Va from the Step 3.
Find V0 from Step 4.
End.

## Slide 23: Adder - Subtractor
  Linear Applications
Home Work
V0 = 6.58V

## Slide 24: Instrumentation Amplifier
  Linear Applications
Instrumentation amplifier is a kind of differential amplifier with additional input buffer stages.
The addition of input buffer stages makes it easy to match (impedance matching) the amplifier with the preceding stage.
Instrumentation are commonly used in industrial test and measurement application.
The instrumentation amplifier also has some useful features,
Low offset voltage
High CMRR (Common mode rejection ratio)
High input resistance
High gain
High accuracy
High gain stability
Low output Resistance etc.

## Slide 25: Instrumentation Amplifier
  Linear Applications

## Slide 26: Instrumentation Amplifier
Working of Instrumentation Amplifier
The output stage of the instrumentation amplifier is a difference amplifier,
Hence, output Vout is the amplified difference of the input signals applied to its input terminals.
The outputs of op-amp 1 and op-amp 2 are Vo1 and Vo2 respectively
Vout = (R3/R2)(Vo1-Vo2)

## Slide 27: Instrumentation Amplifier
Working of Instrumentation Amplifier
Consider the input stage of the instrumentation amplifier,

## Slide 28: Instrumentation Amplifier
Working of Instrumentation Amplifier
The potential at node A is the input voltage V1. Hence the potential at node B is also V1, from the virtual ground concept. Thus, the potential at node G is also V1.
The potential at node D is the input voltage V2. Hence the potential at node C is also V2, from the virtual ground. Thus, the potential at node H is also V2.
Ideally the current to the input stage op-amps is zero. Therefore the current I through the resistors R1, Rgain and R1 remains the same.
Applying Ohm’s law between the nodes E and F,
I = (Vo1-Vo2)/(R1+Rgain+R1)
I = (Vo1-Vo2)/(2R1+Rgain) ——————— 1
Since no current is flowing to the input of the op-amps 1 & 2, the current I between the nodes G and H can be given as,
I = (VG-VH)/Rgain = (V1-V2)/Rgain ————————- 2

## Slide 29: Instrumentation Amplifier
Working of Instrumentation Amplifier
Equating equations 1 and 2,
(Vo1-Vo2)/(2R1+Rgain) = (V1-V2)/Rgain
(Vo1-Vo2) = (2R1+Rgain)(V1-V2)/Rgain —————— 3
The output of the difference amplifier is given as,
Vout = (R3/R2) (Vo1-Vo2)
Therefore, (Vo1 – Vo2) = (R2/R3)Vout —————— 4
Substituting (Vo1 – Vo2) value in the equation 3, we get
(R2/R3)Vout = (2R1+Rgain)(V1-V2)/Rgain
i.e. Vout = (R3/R2){(2R1+Rgain)/Rgain}(V1-V2)
The above equation gives the output voltage of an instrumentation amplifier.
The overall gain of the amplifier is given by the term (R3/R2){(2R1+Rgain)/Rgain}.

## Slide 30: Instrumentation Amplifier
Note:
The overall voltage gain of an instrumentation amplifier can be controlled by adjusting the value of resistor Rgain.
The common mode signal attenuation for the instrumentation amplifier is provided by the difference amplifier.
Advantages of Three Op-amp Instrumentation Amplifier
The gain of a three op-amp instrumentation amplifier circuit can be easily varied and controlled by adjusting the value of Rgain without changing the circuit structure.
The gain of the amplifier depends only on the external resistors used. Hence, it is easy to set the gain accurately by choosing the resistor values carefully.
The input impedance of the instrumentation amplifier is dependent on the non-inverting amplifier circuits in the input stage. The input impedance of a non-inverting amplifier is very high.
The output impedance of the instrumentation amplifier is the output impedance of the difference amplifier, which is very low.
The CMRR of the op-amp 3 is very high and almost all of the common mode signal will be rejected.

## Slide 31: Instrumentation Amplifier
Difference between Operational Amplifier and Instrumentation Amplifier
The key differences between the operational amplifier and instrumentation amplifier include the following.
An operational amplifier (op-amp) is one kind of an integrated circuit
The instrumentation amplifier is one type of differential amplifier
Instrumentation amplifier can be built with three operational amplifiers.
The differential amplifier can be built with a single operational amplifier.
The output voltage of difference amplifier gets affected because of the mismatch resistors
Instrumentation amplifier offers gain with a single resistor of its primary phase which does not need a resistor matching.

## Slide 32: Instrumentation Amplifier
Transducer Bridge Instrumentation Amplifier
Application of Instrumentation Amplifier
Ref.: https://www.electronicshub.org/instrumentation-amplifier-basics-applications/

## Slide 33: Differentiator (Differentiator Amplifier)
Produces a voltage output which is directly proportional to the input voltage’s rate-of-change with respect to time

## Slide 34: Differentiator (Differentiator Amplifier)
Assume it is Ideal Op-Amp, hence,
Current into the terminals are Zero
Input differential Voltage Vd = 0.
Since the node voltage of the operational amplifier at its inverting input terminal is zero, the current, i flowing through the capacitor will be given as
The charge on the capacitor equals Capacitance times Voltage across the capacitor

## Slide 35: Differentiator (Differentiator Amplifier)
Thus the rate of change of this charge is:
but dQ/dt is the capacitor current, i
from which an ideal voltage output for the op-amp differentiator
Vout is a constant –Rƒ*C times the derivative of the input voltage Vin with respect to time. The minus sign (–) indicates a 180o phase shift because the input signal is connected to the inverting input terminal

## Slide 36: Differentiator (Differentiator Amplifier)
Taking Laplace Transform for the above and substitute s = jɷ,

## Slide 37: Differentiator (Differentiator Amplifier)
Drawbacks
Disadvantages of Ideal Differentiator :
The gain of the differentiator increases as frequency increases. Thus at some high frequency, the differentiator may become unstable and break into oscillations.
Also, the input impedance decreases as frequency increases. This makes circuit very much sensitive to the noise .

## Slide 38: Differentiator (Differentiator Amplifier)
Waveforms

## Slide 39: Practical Differentiator
In order to eliminate the
Instability and
High frequency noise
of the basic Differentiator, the Practical Differentiator has existence.

## Slide 40: Practical Differentiator

## Slide 41: Practical Differentiator
The above circuit is similar to Non-Inverting Amplifier,
V0/Vi = - Rf/Ri = -Zf/Z1 ------ (1)
Remember:
Laplace Transform of,
R = R
Cd/dt = 1/sC
From the diagram,
Zf = Parallel Combination of Rf and Cf;
Z1 = Series Combination of R1 and C1.
Zf = Rf || Cf = (Rf/sCf) / (Rf +(1/sCf) ------ (2)
Zf = (Rf) / (1+sRfC1) ------ (3)
Z1 = R1 + (1/sC1) = (1+R1C1s)/sC1 ------ (4)
Sub. (3) and (4) in eqn. (1), we get,
------ (5)

## Slide 42: Practical Differentiator
Sub. R1C1 = RfCf in eqn. (5), we get,
------ (6)
Sub. s = jω and ω = 2Πf in eqn. (6), we get,
------ (7)

## Slide 43: Practical Differentiator
Substituting the values of frequencies fa and fb , the gain A is

## Slide 44: Practical Differentiator

## Slide 45: Practical Differentiator
From the above frequency response,
f < fb, the gain A is increasing at 20dB/decade.
f > fb, the gain A is decreasing at 20dB/decade.
      It is due to R1C1 & RfCf
For a good differentiator,
fa < fb < fc (fc is unity gain-bandwidth of op-amp in Open loop.
T > RfC1
      If, RfC1 > R1C1 & RfCf then it becomes basic Differentiator.

## Slide 46: Practical Differentiator
Problem

## Slide 47: Practical Differentiator
Problem

## Slide 48: Practical Differentiator
Problem

## Slide 49: Practical Differentiator
Problem

## Slide 50: Practical Differentiator
Problem

## Slide 51: Integrator

## Slide 52: Integrator

## Slide 53: Integrator
Taking Laplace Transform for the above and substitute s = jɷ,
or
|A| = fb/f; where, fb = 1/2ΠR1Cf

## Slide 54: Integrator

## Slide 55: Integrator
From the above frequency response,
f = 0, then A is infinite (C does not conduct DC - open loop)
0 < f < fb, the gain A is decreasing at 20dB/decade.
f > fb, the gain A is decreasing at 20dB/decade below Zero.
Issue to be Solved is,
f = 0, then A is infinite (C does not conduct DC - open loop)

## Slide 56: Practical Integrator
In order to avoid the saturation of Integration at low frequencies, an Rf is connected in parallel with Cf.

## Slide 57: Practical Integrator (Lossy)
The Rf and Cf combination dissipates power, that’s why it is called as Lossy Integrator.
The gain at the Low frequency is limited to (-Rf/R1) and Rf = 10 R1. Thus DC stabilization is achieved.
Analysis
The above circuit is similar to Non-Inverting Amplifier,
V0/Vi = - Rf/Ri = -Zf/Z1 ------ (1)
From the diagram,
Zf = Parallel Combination of Rf and Cf;
Z1 = Series Combination of R1 alone.
Zf = Rf || Cf = (Rf/sCf) / (Rf +(1/sCf) ------ (2)
Zf = (Rf) / (1+sRfC1) ------ (3)
Z1 = R1 ------ (4)

## Slide 58: Practical Integrator (Lossy)
Sub. (3) and (4) in eqn. (1), we get,
Analysis
V0 (s) /Vi (s) = - ((Rf/R1) / (1+sRfCf) ------ (5)
Sub. s = jω and ω = 2Πf in eqn. (5), we get,
Sub. fa = 1 / 2ΠRfCf above eqn. becomes,
|A| = - ((Rf/R1) / √(1+(f/fa)2) ------ (6)

## Slide 59: Practical Integrator (Lossy)
Analysis
|A| = - ((Rf/R1) / √(1+(f/fa)2) ------ (6)
1. When f=0 ,the gain |A|=|Rf/R1| —–dc gain 2. When 0<f<fa ,the gain |A|≅|Rf/R1| 3. When f>fa ,the gain |A|≪|Rf/R1| 4. When f= fa , the gain |A|=|Rf/R1 (1/√2) |
Hence, |A|=|0.707 (Rf/R1) |
Consider the following cases:

## Slide 60: Practical Integrator (Lossy)
1. When f=0 ,the gain |A|=|Rf/R1| —–dc gain 2. When 0<f<fa ,the gain |A|≅|Rf/R1| 3. When f>fa ,the gain |A|≪|Rf/R1| 4. When f= fa , the gain |A|=|Rf/R1 (1/√2) |
Hence, |A|=|0.707 (Rf/R1) |

## Slide 61: Practical Integrator (Lossy)
Thus we can have following observations from frequency response of practical integrator:
Bandwidth of practical integrator is fa which is higher than BW of an ideal integrator.
DC gain (at f=0) is |Rf/R1| which is typically ≥10.
For better integration fb ≥ 10fa (99% Accuracy).
For proper integration Time period T of input signal ≥Rf Cf

## Slide 62: Practical Integrator (Lossy)
Problem

## Slide 63: Practical Integrator (Lossy)
Solution

## Slide 64: Practical Integrator (Lossy)
Solution

## Slide 65: Practical Integrator (Lossy)
Solution

## Slide 66: Practical Integrator (Lossy)
Solution

## Slide 67: Practical Integrator (Lossy)
Solution

## Slide 68: Active Filters

## Slide 69: Active Filters
Filters are circuits that are capable of passing signals within a band of frequencies while rejecting or blocking signals of frequencies outside this band. This property of filters is also called “frequency selectivity”.
Filter can be Passive or Active filter.
Passive filters:
The circuits built using RC, RL, or RLC circuits.
Active filters :
The circuits that employ one or more op-amps in the design an addition to resistors and capacitors

## Slide 70: Active Filters
There are two broad categories of filters:
  An analog filter processes continuous-time signals
  A digital filter processes discrete-time signals.
The analog or digital filters can be subdivided into four categories:
Low pass Filters
High pass Filters
Band stop Filters
Band pass Filters

## Slide 71: Active Filters

## Slide 72: Active Filters
Passive Filters Disadvantages:
Made up of passive components - resistors, capacitors and inductors
No amplifying éléments (transistors, op-amps, etc)
No signal gain
1st order - design is simple (just use standard equations to find resonant frequency of the circuit)
2nd order - complex equations
Require no power supplies
Buffer amplifiers might be required
Desirable to use inductors with high quality factors
Inductor
Physical size, and large inductance values are required.
Often prohibitively expensive.
Difficult to implement at frequencies below 1 kHz.
Lossy

## Slide 73: Active Filters
Active Filters Advantages:
No inductors
Made up of op-amps, resistors and capacitors
Provides arbitrary gain
High input impedance prevents excessive loading of the driving source
Low output impedance prevents the filter from being affected by the load
Easy to adjust over a wide frequency range without altering the desired response.
Reduced size and weight
Increased reliability and improved performance

## Slide 74: Active Filters
First Order Low Pass Filter

## Slide 75
V = IR
I = V/R

## Slide 76: Active Filters
Voltage ‘Vin’ as an input voltage signal which is analog in nature.
Voltage ‘Vo’ is the output voltage of the operational amplifier.
Resistors ‘RF’ and ‘R1’ are the negative feedback resistors of the operational amplifier.
There is a single R-C network (marked in the red square) present in the circuit hence the filter is a first-order low pass filter
‘RL’ is the load resistance connected at the op-amp output.
In the circuit we have:

## Slide 77: Active Filters
V0 = (1 + (Rf/Ri))V1 ------ (1)
Apply Nodal eqn. at Node V1,
(V1-Vi)/R + C(dV1/dt) = 0
(V1/R) + C(dV1/dt) = (Vi/R) ---- (2)
Taking Laplace Transform in eqn (2),
(V1(s)/R) + sCV1(s) = Vi(s)/R ---- (3)
Simplifying eqn (3),
V1(s) = Vi(s)/(1+sCR) ---- (4)
V1(s)/Vi(s) = 1/(1+sCR) ---- (5)

## Slide 78: Active Filters
From eqn. (1), the Closed Loop Gain (A0) is,
A0 = V0(s)/ V1(s) = (1 + (Rf/Ri)) ------ (6)
From the diagram, the overall Transfer function is,
H(s) = V0(s)/ Vi(s) = (V0(s)/ V1(s)) . (V1(s)/ Vi(s)) ------ (7)
Using eqn. (5) and (6) in (7) gives,
H(s) = (1 + (Rf/Ri)) /(1+sCR) ------ (8)
Or
H(s) = A0 /(1+sCR) ------ (9)
Where, A0 is Gain of Non-Inverting Amp.
Ref.: https://circuitdigest.com/tutorial/butterworth-filters-first-order-and-second-order-low-pass-butterworth-filters

## Slide 79: Active Filters
H(s) = A0 /(1+sCR) ------ (9)
Sub. ωh = 1/RC in eqn. (9), then,
H(s) = V0(s)/ Vi(s) = A0 /(1+s/ ωh )
H(s) = A0ωh/(ωh+s) ------ (10)
Put s = jω in eqn. (9), then,
H(jω) = A0 /(1+ jωCR) ------ (11)
Use fh = 1/2ΠRC (Cut-off frequency of the Filter) in eqn. (11) then,
H(jω) = A0 /(1+ j(f/fh)) ------ (12)
|H(jω)| = A0 /√(1+ (f/fh)2) ------ (13)

## Slide 80: Active Filters
|H(jω)| = A0 /√(1+ (f/fh)2) ------ (13)
Case i : f << fh (input frequency is very less than the cutoff frequency), ==> |H(jω)| = A0
Case ii : f = fh (input frequency is equal to the cutoff frequency),
==> |H(jω)| = 0.707 A0
Case iii: f > fh (input frequency is higher than the cutoff frequency),
==> |H(jω)| < A0 (20 dB/decade)

## Slide 81: Active Filters
Second Order Low Pass Filter

## Slide 82: Active Filters
V0 = (1 + (Rf/Ri)) VB ------ (1)
A0 = V0/VB = (1 + (Rf/Ri)) ------ (2)
Apply Nodal eqn. at Node A (VA ),
VA (2/R+sC)) = Vi/R+VB/R+V0sC ---- (3)
Second Order Low Pass Filter
For a Non-Inverting Amplifier,
Apply Nodal eqn. at Node B (VB ),
VA/R = VB((1/R)+sC) ---- (4)

## Slide 83: Active Filters
Second Order Low Pass Filter
From eqn. (2),
A0 = V0/VB ------ (2)
VB = V0/A0 ------ (5)
Sub. Eqn. (5) in eqn. (4)
VA = V0/A0(1+sCR) ---- (6)
Sub. Eqn. (6) in eqn. (3)
H(s) = V0/Vi = A0/ (1+sCR(3-A0)+(sCR)2) ---- (7)

## Slide 84: Active Filters
Second Order Low Pass Filter
The Transfer function of 2nd order LPF in terms of ω as,
H(s) = A0ωh2 / (s2+αωhs+(ωh)2) ---- (8)
Or
H(s) = A0 / ((s2/ωh2 ) +(αs/ωh ) +1) ---- (9)
A0 = Gain of Closed loop Amplifier
ωh = Upper Cutoff frequency in rad/sec.
α = Damping Co-efficient
Comparing . Eqn. (7) and eqn. (9)
ωh = 1/RC; or fh = 1/2ΠRC
α = 3-A0

## Slide 85: Active Filters

## Slide 86: Active Filters

## Slide 87: Active Filters
Higher order Butterworth filters are obtained by cascading first and second order Butterworth filters.

## Slide 88: Active Filters
Higher order Butterworth filters are obtained by cascading first and second order Butterworth filters.

## Slide 89: Active Filters
Problem:
Design a 2nd order Butterworth LPF having fh = 1kHz. Discuss the frequency response.

## Slide 90: Active Filters
Solution:
fh = 1/2ΠRC
Assume, C=0.1 µF, then the R is 1.6kΩ.
From the Table, for n=2 (2nd Order), α = 1.414,
hence the Pass band gain A0 = 3-α = 1.586.
A0 = (1 + (Rf/Ri)) = 1.586 and assume, Ri=10kΩ
hence, Rf = 5.86kΩ
Hence the Transfer function is, H(s) = 1.586 / (sn2+1.414sn+1)

## Slide 91: Active Filters
Problem:
Design a 4th order Butterworth LPF having fh = 1kHz. Discuss the frequency response.

## Slide 92: Active Filters
Solution:
fh = 1/2ΠRC
Assume, C=0.1 µF, then the R is 1.6kΩ.
From the Table, for n= 4 (4th Order), α1 = 0.765, α1 = 1.848,
hence the Pass band gain
A01 = 3-α1 = 2.235
A02 = 3-α2 = 1.152
A01 = (1 + (Rf/Ri1)) = 2.235 and assume, Ri1=10kΩ  hence, Rf22 = 12.35kΩ
A02 = (1 + (Rf/Ri2)) = 1.152 and assume, Ri2=100kΩ  hence, Rf2 = 15.2kΩ
Hence the Transfer function is,
H(s) = [2.235 / (sn2+ 0.765 sn+1)]. [1.152 / (sn2+ 1.848 sn+1)]

## Slide 93: Active Filters
Second Order High Pass Filter
Consider R=R1=R2 and C=C1=C2.
Apply the same procedure as discussed for the 2nd Order LPF, and obtain H(s)

## Slide 94: Active Filters
Second Order High Pass Filter
H(s) = V0/Vi = A0/ [1+ ((3-A0)/sCR)+(1/(sCR)2)] ---- (3)
H(s) = A0s2 / (s2+αωls+(ωl)2) ---- (1)
H(s) = A0 / ((ωl2/s2) +(αωl/s) +1) ---- (2)
Or
Comparing . Eqn. (2) and eqn. (3)
ωl = 1/RC; or fl = 1/2ΠRC
α = 3-A0

## Slide 95: Active Filters
Problem:
Design a 2nd order Butterworth HPF having fl = 1kHz. Discuss the frequency response.

## Slide 96: Active Filters
Solution:
fh = 1/2ΠRC
Assume, C=0.1 µF, then the R is 1.6kΩ.
From the Table, for n=2 (2nd Order), α = 1.414,
hence the Pass band gain A0 = 3-α = 1.586.
A0 = (1 + (Rf/Ri)) = 1.586 and assume, Ri=10kΩ
hence, Rf = 5.86kΩ
Hence the Transfer function is, H(s) = 1.586 / (sn2+1.414sn+1)

## Slide 97: Active Filters
Wide Band Pass Filter
First order BPF = Cascade of First order HPF and LPF

## Slide 98: Active Filters
Wide Band Pass Filter
HPF
H(jɷ) = A01(jf/fl) / [1+j(f/fl)]
H(jɷ) = A01(f/fl) / √[1+(f/fl)2] -----(1)
LPF
H(jɷ) = A01 / [1+j(f/fh)]
H(jɷ) = A01 / √[1+(f/fh)2] -----(2)
Total Gain A0 = A01. A02
H(jɷ) = A0 (f/fl)/ √{[1+(f/fh)2]. [1+(f/fl)2 } -----(3)

## Slide 99: Active Filters
Wide Band Reject Filter

## Slide 100: Active Filters
Wide Band Reject Filter

## Slide 101: Active Filters
Design a basic wide-band, RC band stop filter with a lower cut-off frequency of 200Hz and a higher cut-off frequency of 800Hz. Find the geometric center frequency, -3dB bandwidth and Q of the circuit.
Wide Band Reject Filter

## Slide 102: Active Filters
Wide Band Reject Filter

## Slide 103: Active Filters
All Pass Filter
The Other names are,
Phase shift Filters
Constant delay Filters
The phase difference between input and output is CONSTANT among all frequencies.
There are two types,
Phase Lag Filters
Phase Lead Filters
They can be obtained by changing the phase angle between Z1 and Zf.

## Slide 104: Active Filters
All Pass Filter
Feedback and inverting input resistors must be equal to each other
Absolute values of resistors is not critical, but for minimum offset, parallel equivalent of these two resistors should nearly equal the value of R1
Gain of all-pass filter is unity (a necessary condition for normal operation)
By replacing R1 with a potentiometer (or equivalent voltage-controlled resistance), phase angle of output may be varied continuously
Cascading similar all-pass sections produces and additive phase shift
Two all-pass filters cascaded will approach a maximum phase shift of 360°, three sections will approach a maximum phase shift of 540°,..

## Slide 105: Active Filters
All Pass Filter – Phase Lag Filter

## Slide 106: Active Filters
Designed to provide constant gain to signals at all frequencies
Ideally, cover entire frequency spectrum
Flat amplitude response characteristic is quite different from those of other filters (LP, HP, BP, notch)
Produce an output that is shifted in phase relative to input signal
Figure: Output signal lag that of input
For frequencies approaching 0, phase lag approaches 180°
As frequency increases, phase lag of output approaches 0
Phase angle: Ø = -2 tan-1 [2πfRC]
All Pass Filter – Phase Lag Filter

## Slide 107: Active Filters
All Pass Filter – Phase Lag Filter
At node ‘a’,
(Va-Vin/R1) +(Va-V0/Rf) = 0
If R1=Rf then,
(Va-Vin/R1) +(Va-V0/R1) = 0
Vin = 2Va-V0 ------(1)
At node ‘b’,
(Vb-Vin/R) +(Vb-0/(1/sC)) = 0
Vb = Vin/(1+sCR) -----(2)
Va = Vb; hence sub. Eqn. (2) in eqn. (1),
V0 = Vin (1-sCR)/(1+sCR) ----(3)
H(s) = V0/Vin = (1-sCR)/(1+sCR) ----(4)

## Slide 108: Active Filters
All Pass Filter – Phase Lag Filter
H(jω) = V0/Vin = (1-jωCR)/(1+jωCR) ----(4)
Magnitude of |H(jω)| = √{(1+(ωCR)2)/((1+(ωCR)2) = 1
Phase of |H(jω)| = tan-1(-ωCR) - tan-1(ωCR)
= -tan-1(-ωCR) - tan-1(ωCR)
= -2 tan-1(-ωCR)
ϕ= -2 tan-1(f/f0) (ஃ f0=1/2ΠRC)
When, f=0; ϕ= 0°
f=f0; ϕ= -90°
f=α; ϕ= -180°

## Slide 109: Active Filters
All Pass Filter – Phase Lag Filter

## Slide 110: Active Filters
All Pass Filter – Phase Lag Filter

## Slide 111: Active Filters
Designed to provide constant gain to signals at all frequencies
Ideally, cover entire frequency spectrum
Flat amplitude response characteristic is quite different from those of other filters (LP, HP, BP, notch)
Produce an output that is shifted in phase relative to input signal
Figure: Output signal leads that of input
For frequencies approaching 0, phase lead approaches 180°
As frequency increases, phase lead of output approaches 0
Phase angle: Ø = 2 tan-1 [1/(2πfR1C1)]
All Pass Filter – Phase Lead Filter

## Slide 112: Active Filters
At node ‘a’,
(Va-Vin/R1) +(Va-V0/Rf) = 0
If R1=Rf then,
(Va-Vin/R1) +(Va-V0/R1) = 0
Vin = 2Va-V0 ------(1)
At node ‘b’,
(Vb-Vin/(1/sC)) +(Vb-0/(R) = 0
Vb = (sCRVin )/(1+sCR) -----(2)
Va = Vb; hence sub. Eqn. (2) in eqn. (1),
V0 = Vin (-1+sCR)/(1+sCR) ----(3)
H(s) = V0/Vin = (-1+sCR)/(1+sCR) ----(4)
All Pass Filter – Phase Lead Filter

## Slide 113: Active Filters
All Pass Filter – Phase Lead Filter
Magnitude of |H(jω)| = √{(1+(ωCR)2)/((1+(ωCR)2) = 1
Phase of |H(jω)| = tan-1(ωCR/(-1)) - tan-1(ωCR)
= 180°-tan-1(ωCR) - tan-1(ωCR)
ϕ = 180°-2 tan-1(-ωCR)
ϕ= 180°- 2 tan-1(f/f0) (ஃ f0=1/2ΠRC)
When, f=0; ϕ= 180°
f=f0; ϕ= 90°
f=α; ϕ= 0°

## Slide 114: Active Filters
All Pass Filter – Phase Lead Filter

## Slide 115
Comparators
Introduction
A comparator is an electronic circuit, which compares the two inputs that are applied to it and produces an output.
The output value of the comparator indicates which of the inputs is greater or lesser.
Comparator falls under non-linear applications of ICs.
Types of Comparators
Comparators are of two types :
Inverting Comparators
Non-inverting Comparators

## Slide 116
Comparators
Introduction
VIN is less than the DC voltage level at VREF, ( VIN < VREF ). As the non-inverting (positive) input of the comparator is less than the inverting (negative) input, the output will be LOW and at the negative supply voltage, -Vcc resulting in a negative saturation of the output.
If we now increase the input voltage, VIN so that its value is greater than the reference voltage VREF on the inverting input, the output voltage rapidly switches HIGH towards the positive supply voltage, +Vcc resulting in a positive saturation of the output.

## Slide 117
Comparators
Inverting Comparator
An inverting comparator is an op-amp based comparator for which a reference voltage is applied to its non-inverting terminal and the input voltage is applied to its inverting terminal.
The operation of an inverting comparator is very simple. It produces one of the two values, +Vsat and −Vsat at the output based on the values of its input voltage Vi and the reference voltage Vref.

## Slide 118
Comparators
Inverting Comparator
The operation of an inverting comparator is very simple. It produces one of the two values, +Vsat and −Vsat at the output based on the values of its input voltage Vi and the reference voltage Vref.
The output value of an inverting comparator will be −Vsat, for which the input Vi voltage is greater than the reference voltage Vref.
The output value of an inverting comparator will be +Vsat, for which the input Vi is less than the reference voltage Vref.

## Slide 119
The operation of the inverting comparator is;
During the positive half cycle of the sinusoidal input signal, the voltage present at the inverting terminal of op-amp is greater than zero volts. Hence, the output value of the inverting comparator will be equal to −Vsat during positive half cycle of the sinusoidal input signal.
Similarly, during the negative half cycle of the sinusoidal input signal, the voltage present at the inverting terminal of the op-amp is less than zero volts. Hence, the output value of the inverting comparator will be equal to +Vsat during negative half cycle of the sinusoidal input signal.
Comparators
Inverting Comparator
The output transitions either from −Vsat to +Vsat or from +Vsat to −Vsat.
Output changes its value when the input is crossing zero volts.
Hence, the above circuit is also called as inverting zero crossing detector.

## Slide 120
Comparators
Inverting Comparator

## Slide 121
Comparators
Non-Inverting Comparator
A non-inverting comparator is an op-amp based comparator for which a reference voltage is applied to its inverting terminal and the input voltage is applied to its non-inverting terminal.
This op-amp based comparator is called as non-inverting comparator because the input voltage, which has to be compared is applied to the non-inverting terminal of the op-amp.

## Slide 122
Comparators
Non-Inverting Comparator - operation
It produces one of the two values, +Vsat and −Vsat at the output based on the values of input voltage Vt and the reference voltage +Vref.
.
The output value of a non-inverting comparator will be +Vsat , for which the input voltage Vi is greater than the reference voltage +Vref.
The output value of a non-inverting comparator will bee −Vsat, for which the input voltage Vi is less than the reference voltage +Vref.

## Slide 123
Comparators
Non-Inverting Comparator - operation
During the positive half cycle of the sinusoidal input signal, the voltage present at the non-inverting terminal of op-amp is greater than zero volts. Hence, the output value of a non-inverting comparator will be equal to +Vsat during the positive half cycle of the sinusoidal input signal.
Similarly, during the negative half cycle of the sinusoidal input signal, the voltage present at the non-inverting terminal of op-amp is less than zero volts. Hence, the output value of non-inverting comparator will be equal to −Vsat during the negative half cycle of the sinusoidal input signal.
The output transitions either from +Vsat to −Vsat or from −Vsat to +Vsat
The output changes its value when the input is crossing zero volts.
Hence, the above circuit is also called as non-inverting zero crossing detector.

## Slide 124
Comparators
Non-Inverting Comparator - operation

## Slide 125
Comparators
Comparator - Applications
Zero crossing detector
Window Detector
Time Marker generator
Phase meter
Schmitt trigger

## Slide 126
Comparators
Comparator – Zero crossing detector

## Slide 127
Comparators
Comparator – Window Detector
A Window Comparator is basically the inverting and the non-inverting comparators above combined into a single comparator stage.
The window comparator detects input voltage levels that are within a specific band or window of voltages.
Using our idea above of a voltage divider network, if we now use three equal value resistors so that R1 = R2 = R3 = R.
So as the resistive values are all equal, the voltage drops across each resistor will also be equal at one-third the supply voltage, 1/3Vcc.
So for ease in this simple window comparator example, we can set the upper reference voltage to 2/3Vcc and the lower reference voltage to 1/3Vcc.

## Slide 128
Comparators
Comparator – Window Detector

## Slide 129
The inital switching condition of the circuit is the open-collector output of op-amp A1 “OFF” with the open-collector output of op-amp A2, “ON” (sinking current) so VOUT is equal to 0V.
When VIN is below the lower voltage level, VREF(LOWER) which equates to 1/3Vcc, VOUT will be LOW. When VIN exceeds this 1/3Vcc lower voltage level, the first op-amp comparator detects this and switches its open-collector output HIGH. This means that both op-amps have their outputs HIGH at the same time. No current flows through the pull-up resistor RL so VOUT is equal to Vcc.
As VIN continues to increase it passes the upper voltage level, VREF(UPPER) at 2/3Vcc. At this point the second op-amp comparator detects this and switches its output LOW and VOUT becomes equal to 0V.
Then the difference between VREF(UPPER) and VREF(LOWER) (which is 2/3Vccc – 1/3Vcc in this example) creates the switching window for the positive going signal.
Comparators
Comparator – Window Detector
Lets now assume that VIN is at its maximum value and equal to Vcc. As VIN decreases it passes the upper voltage level VREF(UPPER) of the second op-amp comparator which switches the output HIGH. As VIN continues to decrease it passes the lower voltage level, VREF(LOWER) of the first op-amp comparator once again switching the output LOW.
Then the difference between VREF(UPPER) and VREF(LOWER) creates the window for the negative going signal. So we can see that as VIN passes above or passes below the upper and lower reference levels set by the two op-amp comparators, the output signal VOUT will be HIGH or LOW.

## Slide 130
Comparator Voltage Level Detector
Comparators
Comparator – Window Detector

## Slide 131
Comparators
Comparator – Time Marker Generator

## Slide 132
Comparators
Comparator – Time Marker Generator

## Slide 133
Comparators
Comparator – Phase meter / Phase Detector
A zero-crossing detector can be used for the measurement of phase angle between two voltages.
The working will be the same as explained in the Time Marker circuit.
A train of pulses in the positive and negative cycles are obtained and the time interval between the pulse of sine wave voltage and that of second sine wave voltage is measured.
This interval of time is proportional to the phase difference between the two input sine wave voltages. The range of use of phasemeter for measurement is 0° to 360°.

## Slide 134
Comparators
Comparator – Voltage Limiter Circuit Using Op-amp

## Slide 135
At this condition, V0 = VZ + VD1
VZ – Zener Voltage
VD1 – Voltage drop across D1 = 0.7V
If Vo increases from 0 to negative voltage, Vo increases positively until diode D2 is forward biased and D1 goes into avalanche condition.
A t this condition, V0 = VZ + VD2
VZ – Zener Voltage
VD1 – Voltage drop across D2 = 0.7V
Thus the limit of output voltage swing is between +(VZ + 0.7) and –(VZ + 0.7).
When Vin ranges from 0 to positive voltage, D2 is reverse biased and thus V0 = -Vsat.
When Vin ranges from 0 to negative voltage, D2 is forward biased and D1 goes into avalanche condition.
Thus V0 = VZ + VD2.
Comparators
Comparator – Voltage Limiter Circuit Using Op-amp

## Slide 136
Comparators
Comparator – Voltage Limiter Circuit Using Op-amp

## Slide 137
Comparators
Comparator – Voltage Limiter Circuit Using Op-amp

## Slide 138
SCHMITT Trigger
Circuit Diagram
A Schmitt trigger circuit is also called a regenerative comparator circuit.
It is basically an inverting comparator circuit with a positive feedback.
Node ‘A’

## Slide 139
In an Inverting Schmitt Trigger, the input is applied to the inverting terminal of the Op-Amp.
In this mode, the output produced is of opposite polarity.
This output is applied to non-inverting terminal to ensure positive feedback Vref= (βAOL). AOL is the Open Loop Gain of Op-Amp.
SCHMITT Trigger
Operation
The reference voltage VREF and -VREF are called Upper Threshold Voltage VUT and Lower Threshold Voltage VLT.
When VIN is slightly greater than VA, the output becomes -VSAT and if VIN is slightly less that -VA (more negative than -VREF), then output becomes VSAT.
Hence, the output voltage VO is either at VSAT or -VSAT and the input voltage at which these state changes occur can be controlled using R1 and R2.

## Slide 140
SCHMITT Trigger
Analysis
Assume initially, the output V0= +VSAT, then apply nodal analysis at VA,
(VA-VREF)/R2 + (VA-VSAT)/R1 = 0 ----(1)
VA = (R1R2/R1+R2) [VREF/R2+VSAT/R1]
Thus, VUT = (1/R1+R2)[R1VREF+R2VSAT] ----(2)
Similarly, if the output V0= -VSAT, then apply nodal analysis at VA,
(VA-VREF)/R2 + (VA+VSAT)/R1 = 0 ----(3)
VA = (R1R2/R1+R2) [VREF/R2-VSAT/R1]
Thus, VLT = (1/R1+R2)[R1VREF-R2VSAT] ----(4)

## Slide 141
SCHMITT Trigger
Analysis
From eqn. (2) and eqn. (4),
Hysteresis VH = VUT – VLT = (2R2VSAT /R1+R2)
Transfer Characteristic of Schmitt Trigger

## Slide 142
SCHMITT Trigger
Analysis
Consider VREF = 0V then eqn. (2) and eqn. (4) becomes,
VUT = – VLT = (R2VSAT /R1+R2)

## Slide 143
SCHMITT Trigger
Application
One important application of Schmitt Trigger is to convert Sine waves into Square waves.
They can be used to eliminate chatter in Comparators (a phenomenon where multiple output transitions are produced due to swinging of input signal through the threshold region).
They can also act as simple ON / OFF Controllers (for example, temperature based switches).
If we have a noisy input signal as shown figure, the two thresholds of the Schmitt Trigger Circuit will correctly determine the square pulses.
Hence, the basic function of a Schmitt Trigger is to convert noisy square, sine, triangular or any periodic signals into clean square pulses with sharp leading and trailing edges

## Slide 144
SCHMITT Trigger
Non-Inverting Schmitt Trigger Circuit
Problem

## Slide 145
SCHMITT Trigger
Problem

## Slide 146
Astable Multivibrator
Circuit Diagram

## Slide 147
Astable Multivibrator
Output Waveform

## Slide 148
Firstly lets assume that the capacitor is fully discharged and the output of the op-amp is saturated at the positive supply rail.
The capacitor, C starts to charge up from the output voltage, Vout through resistor, R at a rate determined by their RC time constant.
Astable Multivibrator
Operation
RC circuits that the capacitor wants to charge up fully to the value of Vout (which is +V(sat)) within five time constants.
However, as soon as the capacitors charging voltage at the op-amps inverting (-) terminal is equal to or greater than the voltage at the non-inverting terminal (the op-amps output voltage fraction divided between resistors R1 and R2), the output will change state and be driven to the opposing negative supply rail.

## Slide 149
Once the op-amps inverting terminal reaches the new negative reference voltage, -Vref at the non-inverting terminal, the op-amp once again changes state and the output is driven to the opposing supply rail voltage, +V(sat).
The capacitor now see’s a positive voltage across its plates and the charging cycle begins again. Thus, the capacitor is constantly charging and discharging creating an astable op-amp multivibrator output.
Astable Multivibrator
Operation

## Slide 150
Astable Multivibrator
Operation
When power is turned ON, V0 automatically swings either +Vsat or to –Vsat since these are the only stable states allowed by Schmitt trigger. Assume it swings to +Vsat.
Now capacitor starts charging towards +Vsat through the feedback path provided by the resistor R to the inverting input. As long as the capacitor voltage Vc is less than +βVsat, the output voltage remains at +Vsat
As soon as Vc charges to a value slightly greater than +βVsat, the input goes positive with respect to the input. This switches the output voltage from +Vsat to -Vsat
As V0 switches to -Vsat, capacitor starts discharging via . The current I discharges capacitor to 0 V and recharges capacitor to –βVsat. When Vc becomes slightly more negative than the feedback voltage –βVsat, output voltage switches back to +Vsat

## Slide 151
Astable Multivibrator
Analysis
Voltage across Capacitor at time t is given by the eqn. as
Vc(t) = Vf + (Vi - Vf) e(-t/RC) ----(1)
Where Vf is Final Value = +Vsat
Vi is Initial Value = -βVsat
Vc(t) = +Vsat + (-βVsat - Vsat) e(-t/RC) ----(2)
Vc(t) = +Vsat - Vsat(1+β) e(-t/RC) ----(3)
At t= T1, then Vc = +βVsat and Switching Takes place, therefore,
Vc(T1) = βVsat = +Vsat - Vsat(1+β) e(-T1/RC) ----(4)

## Slide 152
Solving eqn. (4) gives,
Astable Multivibrator
Analysis
T1 = RC ln ((1+β)/(1-β)) ----(5)
eqn. (5) for half a cycle, for full cycle,
T = 2T1 = 2RC ln ((1+β)/(1-β)) ----(6)
If R1=R2 then, β = 0.5,
T = 2RC ln 3 ----(7)
If R1=1.16R2 then,
T = 2RC ----(8)
f = 1/2RC ----(9)
Vpp = 2Vsat ----(10)

## Slide 153
Astable Multivibrator
Analysis

## Slide 154
Monostable Multivibrator
Circuit Diagram

## Slide 155
Monostable Multivibrator
Output Waveforms

## Slide 156
Monostable Multivibrator
Operation
The monostable multivibrator is also called as
    One-shot multivibrator
    Time delay circuit
    Gating Circuit
The circuit produces a single pulse of specified duration in response to each external trigger signal. For such a circuit, only one stable state exists.
When an external trigger is applied, the output changes its state. The new state is called as a quasi-stable state. The circuit remains in this state for a fixed interval of time. After some time it returns back to its original stable state.
In fact, an internal trigger signal is generated which drives the circuit back to its original stable state. Usually, the charging and discharging of a capacitor provide this internal trigger signal.

## Slide 157
Monostable Multivibrator
Operation
The diode D1 connected across the capacitor is called clamping diode. It clamps the capacitor voltage to 0.7V when the output is at +Vsat.
A negative triggering pulse is applied to the Non-inverting terminal of Op-amp through RC differentiator circuit and diode D2.
To understand the operation of the circuit, let us assume that the output V0 is at +Vsat i.e. in its stable state.
The diode D1 (Connected across Capacitor) conducts and the voltage across the capacitor C => VC gets clamped to 0.7V Volts.
The voltage at the non-inverting terminal is controlled by voltage divider circuit of R1 and R2.
Voltage at non-inverting terminal (V2) = βV0 {where, β= (R2/(R1+R2))}

## Slide 158
Monostable Multivibrator
Operation
If V1, a negative trigger of amplitude V1 is applied to the non-inverting terminal, so that the effective voltage at this terminal is less than 0.7V. Then the output of the Op-amp changes its state from +Vsat to -Vsat.
The diode is now reverse biased and the capacitor starts charging exponentially to -Vsat through resistance R.
The voltage at the non-inverting terminal is now -βV0.When the capacitor voltage becomes just slightly more negative than -βV0, the output of the Op-amp changes its state back to +V0.
The capacitor now starts charging towards +V0 through R until VC reaches 0.7V as capacitor gets clamped to the voltage.

## Slide 159
Voltage across Capacitor at time t is given by the eqn. as
Vc(t) = Vf + (Vi - Vf) e(-t/RC) ----(1)
Where Vf is Final Value = -Vsat
Vi is Initial Value = VD1
Vc(t) = -Vsat + (VD1 + Vsat) e(-t/RC) ----(2)
At t= T, then Vc = -βVsat and Switching Takes place, therefore,
Vc(T) = --βVsat = -Vsat (VD1 + Vsat) e(-T/RC) ----(3)
Monostable Multivibrator
Analysis

## Slide 160
Monostable Multivibrator
Analysis
Solving eqn. (3) gives,
T1 = RC ln ((1+VD1/Vsat)/(1-β)) ----(4)
If Vsat >> VD1 and R1=R2 then, β = 0.5,
T = 0.69 RC ----(5)
where, β= (R2/(R1+R2))

## Slide 161
Monostable Multivibrator
NOTE:
For Monostable operation, the trigger pulse width Tp should be much less than T.
The diode D2 is not essential but it is used to avoid malfunctioning if any positive noise spikes are present in triggering line.
It can be seen from the waveform that the voltage VC does not reach its quiescent value VD1 until time T’>T. Hence it is necessary that a recovery time (T’>T) be allowed to elapse before the next triggering signal is applied.

## Slide 162
Triangular wave Generator
Method:1
Circuit Diagram

## Slide 163
Triangular wave Generator
Method:1
Circuit Diagram

## Slide 164
Basically, triangular wave is generated by alternatively charging and discharging a capacitor with a constant current.
This is achieved by connecting integrator circuit at the output of square wave generator. Assume that V’ is high at +Vsat.
This forces a constant current (+Vsat / R3) through C (left to right) to drive Vo negative linearly.
When V’ is low at -Vsat, it forces a constant current (-Vsat / R3) through C (right to left) to drive Vo positive, linearly.
The frequency of the triangular wave is same as that of square wave.
Triangular wave Generator
Method:1
Operation
Although the amplitude of the square wave is constant (±Vsat), the amplitude of the triangular wave decreases with an increase in its frequency, and vice versa.
This is because the reactance of capacitor decreases at high frequencies and increases at low frequencies.
In practical circuits, resistance R4 is connected across C to avoid the saturation problem at low frequencies as in the case of practical integrator

## Slide 165
Triangular wave Generator
Method:2
Circuit Diagram
Another triangular wave generator, which requires fewer components

## Slide 166
Triangular wave Generator
Method:2
Operation
It consists of a comparator (A) and an integrator (B).
The output of comparator A is a square wave of amplitude ± Vsat and is applied to the inverting (-) input terminal of the integrator B.
The output of integrator is a triangular wave and it is feedback as input to the comparator A through a voltage divider R2 R3.
To understand circuit operation, assume that the output of comparator A is at + Vsat .
This forces a constant current (+ Vsat / R1) through C to give a negative going ramp at the output of the integrator, as shown in the Fig..
Therefore, one end of voltage divider is at a voltage +Vsat and the other at the negative going ramp.
When the negative going ramp reaches a certain value -Vramp, the effective voltage at point P becomes slightly below 0V.

## Slide 167
Triangular wave Generator
Method:2
Output waveform

## Slide 168
As a result, the output of comparator A switches from positive saturation to negative saturation (-Vsat).
This forces a reverse constant current (right to left) through C to give a positive going ramp at the output of the integrator, as shown in the Fig.
When positive going ramp reaches + Vramp, the effective voltage at point P becomes slightly above 0V.
As a result, the output of comparator A switches from negative saturation to positive saturation (+Vsat).
The sequence then repeats to give triangular wave at the output of integrator B.
Triangular wave Generator
Method:2
Operation

## Slide 169
Triangular wave Generator
Method:2
Amplitude and Frequency Calculation
When comparator output is at +Vsat, the effective voltage at point P is given by
When effective voltage at P becomes equal to zero, we can write above equation

## Slide 170
Similarly, when comparator output is at -Vsat ,we can write,
Triangular wave Generator
Method:2
Amplitude and Frequency Calculation
The peak to peak amplitude of the triangular wave can be given as

## Slide 171
The time taken by the output to swing from – Vramp to + Vramp (or from + Vramp to – Vramp) is equal to half the time period T/2
Triangular wave Generator
Method:2
Amplitude and Frequency Calculation
Substituting value of Vo(pp) we get,
Therefore, the frequency of oscillation can be given as,

## Slide 172
Sine wave Generator
Barkhausen criteria
Electronic oscillators are divided into:
Sinusoidal (or harmonic) oscillators-which produce an output having sine waveform
Non-sinusoidal (or relaxation) oscillator-the output is square, rectangular or saw-tooth or pulse shape.
A(jω)β(jω) = 1(0°)
The total phase shift of the loop gain should be Zero ro multiple of 2Π.
The magnitude of the loop gain Aβ is equal to unity |Aβ| = 1.

## Slide 173
Sine wave Generator
Types of Oscillators
There are two types,
RC Phase Shift Oscillators - Audio Frequencies (Hz to kHz)
LC Oscillators – High Frequencies (in MHz)

## Slide 174
RC Phase Shift Oscillators
Circuit Diagram

## Slide 175
RC Phase Shift Oscillators
Description
R-C phase shift oscillator using op-amp uses an op-amp in inverting amplifier mode. Thus it introduces the phase shift of 180° between input and output. The feedback network consists of 3 RC sections each producing 60° phase shift.
The output of the amplifier is given to the feedback network. The output of the feedback network drives the amplifier. The total phase shift around a loop is 180° of the amplifier and 180° due to 3 RC section, thus 360°. This satisfies the required condition for positive feedback and circuit works as an oscillator.
The gain of the amplifier or op-amp is adjusted with help of Rf and R1 resistances. To get the required oscillations, the gain is adjusted in such a way that the product of op-amp gain and gain of feedback network is slightly greater than 1.

## Slide 176
RC Phase Shift Oscillators
Analysis
Let us find the transfer function of the RC feedback network :

## Slide 177
RC Phase Shift Oscillators
Analysis
Applying KVL to various loops we get,
Replacing jω by s and writing the equations in the matrix form,

## Slide 178
Using the Crammer’s rule to obtain I3
RC Phase Shift Oscillators
Analysis

## Slide 179
RC Phase Shift Oscillators
Analysis

## Slide 180
RC Phase Shift Oscillators
Analysis

## Slide 181
RC Phase Shift Oscillators
Analysis
This is the frequency with which circuit oscillates,
At this frequency, (sub. Α value in β (eqn. 23))
The negative sign indicates a phase shift of 180°

## Slide 182
RC Phase Shift Oscillators
Analysis
Thus circuit will work as an oscillator which will produce a sinusoidal waveform if the gain (A) is 29 and total phase shift around a loop is 360°.
This satisfies the Barkhausen criterion for the oscillator.
These oscillators are used over the audio frequency range i.e. about 20 Hz up to 100 kHz.

## Slide 183
RC Phase Shift Oscillators
Advantages
The circuit is simple to design.
Can produce output over the audio frequency range.
Produces sinusoidal output waveform.
It is a fixed-frequency oscillator.
Disadvantages
By changing the values of R and C, the frequency of the oscillator can be changed. But this is practically impossible. Hence the phase shift oscillator is considered as a fixed frequency oscillator, for all practical purposes.
And the frequency stability is poor due to the changes in the values of various components, due to the effect of temperature, ageing etc.

## Slide 184
RC Phase Shift Oscillators
Problems

## Slide 185
Wien Bridge Oscillators
Circuit Diagram

## Slide 186
Generally in an oscillator, amplifier stage introduces 180° phase shift and feedback network introduces additional 180° phase shift, to obtain a phase shift of 360° around a loop. This is required condition for any oscillator.
Wien Bridge Oscillators
Description
But wiens bridge oscillator uses a non inverting amplifier and hence does not provide any phase shift during amplifier stage. As total phase shift required is 0°, in wiens bridge type no phase shift is necessary through feedback. Thus the total phase shift around a loop is 0°.
The two arms of the bride, namely R1 and C1 in series and R2 and C2 in parallel are called frequency sensitive arms. This is because the components of these two arms decide the frequency of the oscillator.

## Slide 187
Wien Bridge Oscillators
Analysis

## Slide 188
Wien Bridge Oscillators
Analysis
Now replacing

## Slide 189
Wien Bridge Oscillators
Analysis
Substituting the values of and

## Slide 190
Wien Bridge Oscillators
Analysis
Replacing s by jω

## Slide 191
Rationalising the expression
Wien Bridge Oscillators
Analysis
To have zero phase shift of the feedback network, its imaginary part must be zero
This is the frequency of the oscillator and it shows that the components of the frequency sensitive arms are the deciding factors, for the frequency.

## Slide 192
Wien Bridge Oscillators
Analysis
In practice, R1 = R2 = Rand C1 = C2 = C are selected.
Magnitude of the feedback factor at the resonating frequency is ,
β = 1/3
The positive sign of β indicates that the phase shift by the feedback network is 0°. Now to satisfy the barkhausen criterion for the sustained oscillations, we can write,
A = (1+(Rf/R3))
A>3; hence,
(Rf/R3) >2

## Slide 193
Wien Bridge Oscillators
Advantages
Disadvantages
By varying the two capacitor values simultaneously, by mounting them on the common shaft, different frequency ranges can be obtained.
The perfect sine wave output is possible.
It is useful audio frequency range i.e. 20 Hz to 100 kHz.
The frequency stability is poor.

## Slide 194
Precision Diode Rectifiers
General
A rectifier is a circuit that converts alternating current (AC) to Direct current (DC). An alternating current always changes its direction over time, but the direct current flows continuously in one direction. In a typical rectifier circuit, we use diodes to rectify AC to DC. But this rectification method can only be used if the input voltage to the circuit is greater than the forward voltage of the diode which is typically 0.7V.
To overcome this issue, the Precision Rectifier Circuit was introduced. The precision rectifier is another rectifier that converts AC to DC, but in a precision rectifier we use an op-amp to compensate for the voltage drop across the diode, that is why we are not losing the 0.6V or 0.7V voltage drop across the diode,

## Slide 195
Precision Diode Rectifiers
General
When Vout < V’out, diode will be on and the circuit reduces to voltage follower in which Vout = Vin. Because of high gain of op amps the input cut in voltage will be reduced to Vγ/Avo, where Avo is the open loop gain of opamp.
Thus for even for very small input positive voltages the output will be high, the combination of op amp and diode acts as diode with zero cut in voltage hence it is named as precision diode.

## Slide 196
Precision Diode Half Rectifiers
Working

## Slide 197
Observe that the circuit diagram of a half wave rectifier shown above looks like an inverting amplifier, with two diodes D1 and D2 in addition
Precision Diode Half Rectifiers
Working
The working of the half wave rectifier circuit shown above is explained below
For the positive half cycle of the sinusoidal input, the output of the op-amp will be negative. Hence, diode D1 will be forward biased.
When diode D1 is in forward bias, output voltage of the op-amp will be -0.7 V. So, diode D2 will be reverse biased. Hence, the output voltage of the above circuit is zero volts.
Therefore, there is no (zero) output of half wave rectifier for the positive half cycle of a sinusoidal input.
For the negative half cycle of sinusoidal input, the output of the op-amp will be positive. Hence, the diodes D1 and D2 will be reverse biased and forward biased respectively. So, the output voltage of above circuit will be − V0=−(RfR1)V1
Therefore, the output of a half wave rectifier will be a positive half cycle for a negative half cycle of the sinusoidal input.

## Slide 198
Precision Diode Half Rectifiers
Waveforms
As you can see from the above graph, the half wave rectifier circuit diagram that we discussed will produce positive half cycles for negative half cycles of sinusoidal input and zero output for positive half cycles of sinusoidal input

## Slide 199
Precision Diode Full Rectifiers
Working

## Slide 200
Precision Diode Full Rectifiers
Working
For the positive half cycle of a sinusoidal input, the output of the first op-amp will be negative. Hence, diodes D1 and D2 will be forward biased and reverse biased respectively.
Then, the output voltage of the first op-amp will be − V01=−(R2/R1)Vi
Observe that the output of the first op-amp is connected to a resistor R4, which is connected to the inverting terminal of the second op-amp. The voltage present at the non-inverting terminal of second op-amp is 0 V. So, the second op-amp with resistors, R4 and R4 acts as an inverting amplifier.
The output voltage of the second op-amp will be V0=−(R5/R4)V01
Substituting the value of V01 in the above equation, we get −
=>V0=−(R5/R4){−(R2/R1)Vi}
=>V0=(R2R5/R1R4)Vi
Therefore, the output of a full wave rectifier will be a positive half cycle for the positive half cycle of a sinusoidal input. In this case, the gain of the output is R2R5R1R4
If we consider R1=R2=R4=R5=R, then the gain of the output will be one.

## Slide 201
For the negative half cycle of a sinusoidal input, the output of the first op-amp will be positive. Hence, diodes D1 and D2 will be reverse biased and forward biased respectively.
The output voltage of the first op-amp will be − V01=−(R3/R1)Vi
The output of the first op-amp is directly connected to the non-inverting terminal of the second op-amp. Now, the second op-amp with resistors, R4 and R5 acts as a non-inverting amplifier.
The output voltage of the second op-amp will be −
V0=(1+R5/R4)V01
Substituting the value of V01 in the above equation, we get
=>V0=(1+R5/R4){−(R3/R1)Vi}
=>V0=−(R3/R1)(1+R5/R4)Vi
Therefore, the output of a full wave rectifier will be a positive half cycle for the negative half cycle of sinusoidal input also. In this case, the magnitude of the gain of the output is (R3/R1)(1+R5/R4)
. If we consider R1=2R3=R4=R5=R then the gain of the output will be one.
Precision Diode Full Rectifiers
Working

## Slide 202
Precision Diode Full Rectifiers
Waveforms
The full wave rectifier circuit diagram that we considered will produce only positive half cycles for both positive and negative half cycles of a sinusoidal input.

## Slide 203
Precision Diode Peak Detector
Working

## Slide 204
Peak detector detects and holds the most positive value of attained by the input signal prior to the time when the switch is closed.
Precision Diode Peak Detector
Working
Let us consider initially the capacitor is charged to voltage Vc.
The diode employed in the circuit gets forward biased when the applied input voltage Vin exceeds the capacitor voltage Vc. Thereby allowing the circuit to behave as a voltage follower. The output voltage follows the applied input voltage until Vin is more than Vc.
As the input voltage Vin reduces below the value of capacitive voltage Vc, it causes the diode to get reverse biased. In such condition, the capacitor retains the value until the input again exceeds the value stored in the capacitor
As it is a positive peak detector, one can also construct a negative peak detector circuit, that will hold the lowest or most negative signal voltage. This is basically done by reversing the polarities of the diode in the circuit.

## Slide 205
Precision Diode Clippers
General
Wave shaping circuits are the electronic circuits, which produce the desired shape at the output from the applied input wave form. These circuits perform two functions −
Attenuate the applied wave
Alter the dc level of the applied wave.
There are two types of wave shaping circuits: Clippers and Clampers.
A clipper is an electronic circuit that produces an output by removing a part of the input above or below a reference value. That means, the output of a clipper will be same as that of the input for other than the clipped part. Due to this, the peak to peak amplitude of the output of a clipper will be always less than that of the input.
Clippers can be classified into the following two types based on the clipping portion of the input.
Positive Clipper
Negative Clipper

## Slide 206
Precision Diode Clippers
Positive Clipper

## Slide 207
A positive clipper is a clipper that clips only the positive portion(s) of the input signal.
A sinusoidal voltage signal Vi is applied to the non-inverting terminal of the op-amp. The value of the reference voltage Vref can be chosen by varying the resistor R2.
The operation of the circuit shown above is explained below −
If the value of the input voltage Vi is less than the value of the reference voltage Vref, then the diode D1 conducts. Then, the circuit given above behaves as a voltage follower. Therefore, the output voltage V0 of the above circuit will be same as that of the input voltage Vi, for Vi < Vref
If the value of the input voltage Vi is greater than the value of reference voltage Vref, then the diode D1 will be off. Now, the op-amp operates in an open loop since the feedback path was open. Therefore, the output voltage V0 of the above circuit will be equal to the value of the reference voltage Vref, for Vi > Vref.
Precision Diode Clippers
Positive Clipper

## Slide 208
Precision Diode Clippers
Positive Clipper

## Slide 209
Precision Diode Clippers
Negative Clipper

## Slide 210
Precision Diode Clippers
Negative Clipper
A negative clipper is a clipper that clips only the negative portion(s) of the input signal. You can obtain the circuit of the negative clipper just by reversing the diode and taking the reverse polarity of the reference voltage, in the circuit that you have seen for a positive clipper.
The operation of a negative clipper circuit is explained below −
If the value of the input voltage Vi is greater than the value of reference voltage Vref, then the diode D1 conducts. Then, the above circuit behaves as a voltage follower. Therefore, the output voltage V0 of the above circuit will be same as that of the input voltage Vi for Vi> Vref
.
If the value of the input voltage Vi is less than the value of reference voltage , then the diode D1 will be off. Now, the op-amp operates in an open loop since the feedback path is open. Therefore, the output voltage V0 of the above circuit will be equal to the value of reference voltage ,Vref for Vi < Vref

## Slide 211
Precision Diode Clippers
Negative Clipper

## Slide 212
Precision Diode Clampers
General
A clamper is an electronic circuit that produces an output, which is similar to the input but with a shift in the DC level. In other words, the output of a clamper is an exact replica of the input. Hence, the peak to peak amplitude of the output of a clamper will be always equal to that of the input.
Clampers are used to introduce or restore the DC level of input signal at the output. There are two types of op-amp based clampers based on the DC shift of the input.
  Positive Clamper
  Negative Clamper

## Slide 213
Precision Diode Clampers
Positive Clamper

## Slide 214
A positive clamper is a clamper circuit that produces an output in such a way that the input signal gets shifted vertically by a positive DC value.
Precision Diode Clampers
Positive Clamper
A sinusoidal voltage signal, Vi is applied to the inverting terminal of op-amp through a network that consists of a capacitor C1 and a resistor R1 That means, AC voltage signal is applied to the inverting terminal of the op-amp.
The DC reference voltage Vref is applied to the non-inverting terminal of the op-amp. The value of reference voltage Vref can be chosen by varying the resistor R2. In this case, we will get a reference voltage Vref of a positive value.
The above circuit produces an output, which is the combination (resultant sum) of the sinusoidal voltage signal Vi and the reference voltage Vref. That means, the clamper circuit produces an output in such a way that the sinusoidal voltage signal Vi gets shifted vertically upwards by the value of reference voltage Vref

## Slide 215
Precision Diode Clampers
Positive Clamper
The positive clamper shifts the applied input waveform vertically upward at the output. The amount of shift will depend on the value of the DC reference voltage.

## Slide 216
A negative clamper is a clamper circuit that produces an output in such a way that the input signal gets shifted vertically by a negative DC value.
Precision Diode Clampers
Negative Clamper

## Slide 217
The negative clamper shifts the applied input waveform vertically downward at the output. The amount of shifting will depend on the value of DC reference voltage
Precision Diode Clampers
Negative Clamper